## Slide 1: New Code Base
Paul Pridham
9/14/2022

## Slide 2: Why New Code?
Nano:
  Pro: has built in Bluetooth
  Con: Slow clock
  Con: Noisy ADC
Teensy:
  Pro: Fast Clock
  Pro: Good ADC
  Con: Needs external Bluetooth that can cause controls to hang while message is being sent
Each controllers’ cons are not an issue with the other so by having the Teensy offload Bluetooth communication to the Nano we should end up with an overall faster system
Expected possible control loop speed is ~600µs for 4 motors using 2 CAN busses and custom libraries.

## Slide 3: Overview

## Slide 4: UI Host
Interface the user touches, app on phone or tablet
Packages and sends individual Bluetooth messages.

## Slide 5: Nano
Handles Bluetooth communication
Mirrors ExoData stored on the Teensy
Handles low frequency sensor reading

## Slide 6: Teensy
Handles most of the computation
Configures System
Does primary sensor readings
  FSR
  Torque Sensors
Does primary output
  Motors
  Sync LED
  Status LED

## Slide 7: ExoData
Stores the data and parameters used to control the system
Mirrors setup of Exo

## Slide 8: Exo
Handles the computation
Reads sensors and puts data in ExoData instance.
  FSR
  Torque Sensors
Calculates output commands and sends to components
  Motors
  Sync LED
  Status LED

## Slide 9: SD Card
Stores system configuration
Till app fully set up:
  Contains parameter sets for different controllers.

## Slide 10: Motors
Currently CAN motors but other types can be added
Takes in torque commands

## Slide 11: Torque Sensors
Measures torques at the joint
Controllers have flag to use PID
  Select if torque sensor present
  Don’t use if there is no torque sensor

## Slide 12: FSR
Used to determine pressure at the heel and toe.
Used to determine foot strike and percent gait based on that.
Some controllers use one or both of these sensors.

## Slide 13: Status LED
Displays messages based on exoskeleton status.
  Colors (RGB)
  Patterns
    Solid (Color)
    Blink (Color, Freq)
    Pulse (Color, Freq)
    Rainbow (Freq)

## Slide 14: Sync LED
Used to synchronize the exoskeleton with infrared(IR) motion capture through an IR LED
Pulse Pattern
  Long pulse at start and end
  Small pulses in middle

## Slide 15: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
* These loops happen regardless of trial state
  100 Hz*
  Teensy pulls updated app info from Nano
  Teensy pushes data to Nano
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led

## Slide 16: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
* These loops happen regardless of trial state
  100 Hz*
  Teensy pulls updated app info from Nano
  Teensy pushes data to Nano
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led

## Slide 17: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
* These loops happen regardless of trial state
  100 Hz*
  Teensy pulls updated app info from Nano
  Teensy pushes data to Nano
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led

## Slide 18: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
* These loops happen regardless of trial state
  100 Hz*
  Teensy pulls updated app info from Nano
  Teensy pushes data to Nano
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led

## Slide 19: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
* These loops happen regardless of trial state
  100 Hz*
  Teensy pulls updated app info from Nano
  Teensy pushes data to Nano
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led

## Slide 20: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
* These loops happen regardless of trial state
  100 Hz*
  Teensy pulls updated app info from Nano
  Teensy pushes data to Nano
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led

## Slide 21: Concept of Operations
Check/update configuration on the SD Card
Turn on
Teensy reads config
  Sends info to Nano
Both boards create ExoData object
Teensy creates Exo object
Calibrates sensors
Select controllers to use for the joints
Start trial
End trial
  100 Hz*
  Nano pushes updated app info to the Teensy
  Nano pulls new sensor data from the Teensy
  Nano updates app
  500+ Hz*
  Teensy reads data from sensors
  Teensy updates motor commands/Sync Led
* These loops happen regardless of trial state

## Slide 22
Code Location
  https://github.com/naubiomech/ExoCode/tree/nano_teensy_board
User Guide
  https://github.com/naubiomech/ExoCode/tree/nano_teensy_board/Documentation