## Slide 1: 半导体界统计和R的应用
中芯国际 －良率管理系统
2008-12-13

## Slide 2: Content
Background
R Usage at SMIC

## Slide 3: Integrated Circuit (IC) Manufacturing
CD SEM
Overlay
Macro
CD SEM
Films
Stepper / Track
Etch
Etcher
5XXX
8XXX
ASET-F5
2401
Hitachi
Films
Dep
2. IC Manufacturing
1. IC Design
N-Well
P-Well
P+
P+
N+
N+
Metal 1
3. Fabricated Wafers

## Slide 4: Semiconductor Data Flow
WAT
FT
WS/CP
WIP (MES, iEMS)
Wafer
start
Fab out
Continually Defect inspection and review:
inspection tool KLA,compass) review tool: SEM Leica(OM)
Continually ADI, AEI, CD,etc measurement called metrology
(MES)
MET
Defect
(KLARF)
WIP
EQ log
data
Test data
Process data
Also reliability, memory bit, QC and other data

## Slide 5: Statisticians at SMIC
Reliability Analysis
Quality Control
Price
Time to Market
Original Yield Ramp
Our Mission:
Improved Yield Ramp
Yield Analysis

## Slide 6: R Usage at SMIC
1、线性模型/非线性模型/广义线性模型
  Linear model for inline monitor
  Basic mixed effect model applied to semiconductor data
  Various correlation analyses
2、统计图形：阐述清楚统计原理与图形元素的对应关系
  Useful and interesting plots: histogram w/ splits, plot w/ table (Excel like), wafer map (3-D)
3、非参数统计：各种基于秩的检验以及光滑方法
  Smooth spline usage, EWMA Control Chart
5、多元统计：一方面展示已有方法的应用，如主成分、聚类等，另一方面体现出R在矩阵运算方面的简便
  Wafer pattern classification: clustering analysis
7、数据挖掘和机器学习: Logistic回归、kNN、以及神经网络、SVM等
  Logistic regression application
9、程序接口：C/Fortran/C++/Java等或者R (D)COM、Rserve
  Python / VB / Delphi / mySQL linking with R
  R (D)COM under study

## Slide 7: Climb the Mountain Peak of R, Fighting !!!

## Slide 8
Thank you 谢谢
Q&A 请您提问

## Slide 9: Linear Model for Inline Monitor
  Inline analysis objectives
    Automatically examine ALL metrology items
    Alarm only significant trends and related equipment
Drill Down
A
B

## Slide 10: WAT Uniformity Analysis (Mixed Effects Model Example)
Problem Description:
Break WAT parameters variation into lot, wafer & die components;
Highlight large or increasing variance contributors to better control the manufacturing process.
i: lot number 1,2,…a; j: wafer number 1,2,…b; k: site number 1,2,…n.
Reference Book : Mixed Effects Models in S and S-Plus.
Analysis Method:
Mixed Effects Model: three-level nested linear model;
Applied areas: agriculture, biology, economics, manufacturing & geophysics
Using R (nlme), lot, wafer & die variance components are estimated.

## Slide 11: WAT Uniformity Analysis Example Result
Obs
Component
Var Component
% of Total
Sqrt(Var Comp)
1
Lot
0.225
31.6
0.475
2
Wafer
0.419
58.8
0.648
3
Die
0.068
9.6
0.262
4
Total
0.713
100.0
0.844

## Slide 12: Other Correlation Analyses
Equipment Comparison
9 days
12 days
Queue Time

## Slide 13: Interesting Plot 1
Histogram plot

## Slide 14: Interesting Plot 2
Wafer Map
Notes: hhhhhh

## Slide 15: Smooth Spline Usage
Split
Reduce noise
Split control limit
  Smooth spline simulates the data for
  reducing noise

## Slide 16: EWMA Control Chart
The Purpose of EWMA Control Chart:
Detect data trend shift ;
Reduce SPC X-bar chart's excursion false alarm rate.

## Slide 17: Cluster Analysis
Block issue
Serious edge issue
Used “neural network like” methods
Periodic fail pattern
Composite wafers analysis
Cluster fail pattern
Continuous fail pattern
Periodic pattern
Continuous fail

## Slide 18: Illustrations for Single Wafer Analysis
Continuous fail
Zone pattern
Single wafer analysis
Cluster single & multi bin
Reticle/DUT pattern
Zone pattern
Continuous fail
Cluster fail
Reticle fail

## Slide 19: Procedure Interface / Data Preparation
Procedure Interface :
Python ( Perl ) / VB / Delphi / mySQL linking with R. ( Studying )
Data Convert :
Common use：reshape, merge, sort / order, apply, as.POSIXct….
Purpose：match the format of SMIC data analysis systems .
Data Clean :
Wipe off the influential point , missing data ….
Purpose： prevent “ Garbage In , Garbage out ” .